Wireless Keylogger
Brian Crone
Evan Graves
Samuel Oshin
Yonatan Feleke

---
Project Overview of Wireless Keylogger
- The Wireless Keylogger will be able to monitor keystrokes entered on a target keyboard
- It will be equipped with DES encryption to avoid just anyone from accessing the contents of the SRAM
- Data would be transmitted wirelessly to keep its presence discreet.
- Features:
  - USB Interface
  - Encryption of Keystrokes
  - Off Chip SRAM Storage
  - Bluetooth Wireless transfer

---
System Level Diagram
Wireless Keylogger
Wireless Receiver
Host Computer
Keyboard
USB
USB
Bluetooth

---
Architecture Diagram
USB RECIEVER
ENCRYPTION
MEMORY
BLUETOOTH
RECIEVER
Full
Empty
Data
r_enable
Full
Empty
Data
r_enable
r_enable
Data
Antenna
Power
Ground
D+
D-
Keyboard
Host
Computer
R_ERROR

---
Sequence Flowchart
Data Packet
Transmit to Receiver
Store in Off Chip SRAM
Read from SRAM
Encrypt
Listening on USB line
Transmit Packet?
Listen on Bluetooth
Output to Screen
Yes
Yes
No
No

---
DECODE
SHIFT_REG
W/ BIT STUFFING
TIMER
EDGE_DETECT
CRC REGISTER
(MODIFIED SHIFT
REGISTER)
RCV_FIFO
EOP_DETECT
(COMBINATIONAL)
RCU
(FSM)
CLOCK DIVIDER
/3
D_PLUS
D_MINUS
EOP
D_EDGE
D_EDGE
D_PLUS
EOP
DATA
W_ENABLE
R_ENABLE
RCV_DATA[7:0]
CRC_ERROR
SHIFT
D_ORIG
SHIFT_ENABLE
CLK
RST
RCLK
R_DATA[7:0]
EMPTY
R_ERROR
FULL
RCVING
USB RECEIVER
RCVING

---
TIMER
TIMER NEXT STATE LOGIC
TIMER STATE REG.
TIMER OUTPUT LOGIC
nextstate[3:0]
clk
rst
State[3:0]
D_EDGE
RCVING
SHIFT_ENABLE
Description:
Strobe SHIFT_ENABLE every 8 clock cycles (12 Mb/s)
If an edge is detected, timer will resynchronize start its count over. It will wait 3 cycles, strobe SHIFT_ENABLE, then restart its 8 count.

---
DECODE
DECODE NEXT STATE LOGIC
DECODE STATE REG.
DECODE OUTPUT LOGIC
nextstate[1:0]
clk
rst
State[1:0]
EOP
SHIFT_ENABLE
D_ORIG
Description:
Samples the D_PLUS line when SHIFT_ENABLE is asserted high
If there is a transition in the D_PLUS line, D_ORIG will be asserted low. No transition will result in D_ORIG being asserted high.
D_PLUS
SHIFT_ENABLE

---
EDGE DETECT
EDGE NEXT STATE LOGIC
EDGE STATE REG.
nextstate
clk
rst
D_EDGE
D_PLUS
x
EOP DETECT
D_PLUS
D_MINUS
EOP
Description:
Edge Detect will strobe high when it detects a high to low or low to high transition on D_PLUS.
Description:
EOP Detect will set the EOP signal when both D_PLUS and D_MINUS are set low simultaneously.

---
Register
IF 1_ctr = 6
 Then
RCV_DATA
ELSE
  RCV_DATA[7:1]
& D_Orig
IF D_Orig = 1 then 1_ctr++
ELSE 1_ctr = 0
D_Orig
D_Orig
RCV_DATA
nextRCV_DATA
Shift Register w/ Bit Stuffing
Description:
Shifts in serial data to a 8-bit parallel out
If it receives 6 consecutive 1’s, the shift register will ignore the next shift command and not shift in the next data bit (which will be a zero)
SHIFT_ENABLE

---
Receive
First Byte
Receive PID Byte
Receive
Next Data Byte
Load Byte
Into FIFO
Sync Byte?
PID: Data Type?
EOP?
Does CRC Agree?
Error.
Ignore Packet
YES
YES
YES
YES
NO
NO
NO

---
Encryption block, gets the data, 64 bits at a time, encrypts and stores in a fifo to be stored in memory.
Fiestel Function
ENC_Controller
Round Key Gen
1 0
1 0
Fiestel Register
Round Counter
FIFO
clk
RndCt
clk
Data
Full
Empty
Enc_Left
Start
Enc_Right
R_enable
W_enable
F_R
F_L
R_Key
In_Select
F_R
F_L
Data
Encryption Block

---
Generates the Round Key, by using the key in halves, shifting them determined by the round counter, and Permuted twice.
Shift
PBOX1
PBOX2
LH
Rnd_#
RH
Rnd_#
LH_S
RH_S
P1_LH
P1_RH
P2_LH
P2_RH
1 0
1 0
Enc_Left
Enc_Right
F_R
F_L
Round Key Gen
32
32
32
32
32
32
32
32
32
32

---
Basic functions outline in the Fiestel Function, Expansion permutation, Xor with Round Key, Substitution Box, and Permutation Box.
EXP_PERM
SBOX
HDATA
EXP_DATA
SDATA
XORDATA
RKEY
PBOX
PDATA
32
32
32
32
Fiestel Function

---
ENC Controller is used to control the function of the encryption block, it sends a start signal, a w_enable and also a r_enable.
0 1
 State Register
If X< 8 then X+1 else 0
Compile Block
Empty
start
0
clk
Empty
start
DataAll
w_enable
Data
r_enable
64
8
3
ENC Controller

---
Compile Block compiles the 8 by 8 Fifo provided by the USB receiving block, into a single 64 bit Data, and also includes a timer to count how long it will take for the encryption to be done.
Shifts data according to count
CNT16State REgister
If X < 16 then X + 1 else 0
0 1
Start
Cnt
Data
DataAll
Cnt
Clk
0
Cnt
w_enable
DataAll (63:32)
DataAll (31:0)
64
4
Compile Block

---
Round counter increments from 0 to 15, identifying all rounds of a typical DES encryption. The In_Select is used to choose the inputs for encryption (once past 0 it should use the previous output)
0 1
 State Register
If X< 16 then X+1 else 0
0
clk
Empty
Empty
In_Select
Rnd_Cnt
4
Round Counter

---
Memory
Memory receives a Full or Empty signal from the Encryption block. Memory doesn’t start reading in the Encrypted data until the Full strobe is asserted. Once the data is read in, the data is stored in the SRAM if the Read_enable signal from the Bluetooth is high. The Bluetooth then can receive 256 bits of stored memory.

---
Bluetooth Send Block
CLK
RST
B_AppendAcessCode
B_UAT
ACESS_CODE(72)
Reg
DATAOUT
B_StripPayload
BLUE_EN
EMPTY
ANT_LOUT
ANT_INR
READ_EN1
err
HEADER_EN
REPLY_EN
B_HeaderGen
B_nextpacket
HEADER(54)
Reg
TRANS_EN
ANT_ROUT
ENCODE_EN
ESTORE_EN
B_EncodePacket
READ_EN
PAYLOAD(8)
data
NEXT_EN
B_Controller
RESEND_EN
EMPTY
ANT_LIN
The Bluetooth send block utilizes a section OBEX file transfer protocol. The way it gets implemented is that when a send packet is received from a Bluetooth device the process block sends out the data packet. Since 474 bytes are supported on one transmission we are assuming that only one send sequence is going to occur. The various Bluetooth inticate details are accomplished via the gen blocks.

---
EncodeEN
EncodePacket
Clk
rst
CounterReg
NextState
If(ctr<256)
    Ctr+1
    If data change
       Trans++
data
CRC
Reg
Transs
OutputLogic
If ctr= 340
Trans=CRC
Prefix=
   Append 00001
   Append 256
counter
Appendtodata
data
Packet
This encoding is to append a crc to the end of the data that has been inputed into the system. And append a slave ID for an L_CH value(4bits), insert a Flow bit(1 bit) and the length of the datastream which will be a constant 256 in binary(8bits) and then the 256 bit data followed by a 16 bit crc. Total of 285 bits.
prefix
CRC
NextState
storeEN

---
StartChk
ShifRegister
Clk
rst
Rx
Reg
RxData
outputLogic
State
TransEN
nxtStateLogic
Clk
rst
Clk
rst
resendEN
The StartChk block is a serial receiver that waits for a send or resend packet from a hardocoded addressed Bluetooth device. When resend asser both resendEN and TransEN. Else assert only TransEN
empty

---
Universal Asynchronous Transmit
Timer
Strobe on every 656 clock cycles to bring clk =288 mHZ to the data
Rate of 439 Kb/s
Shiftout
16 bit parallel to serial output
SRAM
384bit
Clk
rst
Clk
rst
accesscode
header
data
ANT 440 kb/s
Strobe
packet
Stop Send
This block gets the compiled packet and then sends it out serially over the Bluetooth wire for processing. It utilizes an 8bit parallel to serial convertor that is strobed by a clock divider to match transmit speed. It is also controlled via the SRAM controller to shift out all 384 bits that comprise one packet.
sendEN
renable
SendEN
Clk
rst
StateReg
NextState
SRMCont
Put 16 bits on the bus
Output
Logic
empty
nxtstate
state

---
StripPayload
Clk
rst
CounterReg
NextState
If(ctr<16)
   Ctr+1
   If data change
       Trans+1
RXData
CRC
Reg
Transs
OutputLogic
If ctr= 340
 If Trans=RxDat
     Resend=0
 Else resend=1
 storeEn1 = 1
Else
  storeEN2=1
counter
Resend
Stripayload block removes all the header information (ignores the first first 122 bits) and then calculates the CRC of the data that was passed 16 bits at a time 32 times and compares that to the CRC appended to the data field (very last 16 bit data). If discrepancies are present then the err flag is set.
ShifReg
16bit
Clk
rst
Rx
Clk
rst
CounterReg
NextState
If(ctr<122)
    Ctr+1
Else
    EN=1
counter
EN
Stripfirs122
RxData
SRAM
256 bit
storeEN1
data
RxData

---
0 1
nextpacket
ResendPacketReg
SendPacketReg
Err
Clk
rst
Clk
rst
shiftout
rst
resendp
sendp
Tx
Packet
This block normalizes the clock to the reverse transmit speed and then if error -> sends the resend packet and if not error then sends the send new packet. Shifts out the parallel packet value
Timer
Strobe on every k clock cycles
Strobe
Clk
rst

---
Area and Timing Budget Overview
- Total estimated core area: 2,634,750 um2
- Total available chip area is 7,413,807.189 um2
- Leaves plenty of room for unforeseen additions
- Timing Concerns:
  - Fiestel Register has 1512 gates and will have large propagation delay
  - StripPayload Counter Reg out will also have a large propagation delay
  - But because we are collecting keystrokes, the timing delays are not of as a big concern as area